## Slide 1
MINI PROJECT / MICROPROCESSORS AND MICROCONTROLLERS
8051 Hardware Lab
Real-time embedded monitoring on the AT89S52
From browser simulator to measured silicon in one build cycle
Authors ATHARVA (24BEL0082) - ADITYA (24BEL0087)
Department Electronics and Communication Engineering
Academic year 2025 - 26
Review Technical Review Committee
Artifacts Schematic, BOM, 13 Keil C51 programs, test report
AT89S52
SYSTEM ID
Target AT89S52-24PU
Clock 11.0592 MHz
Bus 8-bit shared, P0
Firmware Keil C51, 13 programs
32 / 32
I/O PINS UTILISED
full allocation, no headroom
0.00 %
UART BAUD ERROR
TH1 = FDH at 11.0592 MHz
0.78 C
ADC RESOLUTION
Vref/2 trimmed to 1.000 V
INR 985
BOM PER BOARD
through-hole, single unit

## Slide 2
SLIDE 02 / PROBLEM
Problem statement and constraints
What had to be solved before a single component was placed
PROBLEM STATEMENT
Transfer the verified 8051 programs from a software model onto a physical AT89S52, interfacing eight LEDs, a two digit seven segment display, a 16x2 character LCD, an eight way DIP switch bank, an LM35 temperature sensor through an ADC0804, a MAX232 serial link, a relay and a buzzer, and confirm on the bench that every output matches the value the simulator predicted.
Hard constraint:
the peripherals require 54 I/O lines and the 8051 provides 32. The architecture must close a 22 pin deficit without adding a port expander IC.
DESIGN CONSTRAINTS
I/O budget 54 required, 32 available
Port 0 topology open drain, cannot source
Latch read-back no read path to the latches
ISP contention P1.5-P1.7 shared with SPI
ADC resolution 8 bits, reference is a choice
No HW debounce buttons bounce 1 to 10 ms
ID | Constraint | Consequence if ignored | Mitigation in this design
C1 | 32 I/O pins for 54 signals | peripherals dropped, or an expander IC added | single 8-bit bus on P0 with per-device strobes on P2
C2 | P0 is open drain | the bus never reaches a valid logic 1 | RN1, a 10 kOhm x 9 SIP network, pulls the bus up
C3 | Output latches cannot be read | a stale byte is latched into the wrong device | bus_shadow variable plus interrupt gating on transfers
C4 | SW6-SW8 share the ISP lines | in-circuit programming fails or is corrupted | 1 kOhm series resistors and a documented OFF state
C5 | 8-bit ADC, 5 V default reference | 1.95 C per step, most of the range wasted | Vref/2 trimmed to 1.000 V, giving 0.78 C per step
C6 | No hardware debounce on the buttons | one press registers as several interrupts | 5 ms resampling and edge triggered IT0 and IT1
8051 HARDWARE LAB / ECE 2025-26
constraint register C1-C6
02 / 07

## Slide 3
SLIDE 03 / ARCHITECTURE
System block diagram
One shared 8-bit bus resolves the 22 pin deficit
AT89S52-24PU
40-pin DIP / 11.0592 MHz
SW1 8-way DIP
P1.0-P1.7
PB1 / PB2
P3.2 / P3.3
LM35 sensor
ADC Vin+
Relay + buzzer
P3.4 / P3.5
Digit selects
P3.6 / P3.7
MAX232 / DB9
P3.0 / P3.1
BD0 - BD7 shared 8-bit data bus port 0 10 kOhm pull-ups
U2 74HC573
8 LEDs
P2.0 LED_LE
U3 74HC573
7-segment x2
P2.1 SEG_LE
LCD1 16x2
HD44780 8-bit
P2.2-P2.4 E RS RW
U4 ADC0804
LM35 8-bit
P2.5-P2.7 WR RD INTR
Interface | Width | Signals | Direction | Device
Parallel bus | 8 bit | BD0-BD7 | bidirectional | U2 U3 LCD1 U4
Latch strobe | 1 bit | LED_LE SEG_LE | output | U2 U3
LCD control | 3 bit | E RS RW | output | LCD1
ADC control | 3 bit | WR RD INTR | in / out | U4
Serial + GPIO | 6 bit | TxD RxD P3.4-P3.7 | both | MAX232 Q1-Q4
PIN ECONOMY
54 pins required -> 32 available
Three 8-bit data paths merged into one bus, saving 24 pins.
Eight of them pay for the strobes. Net saving: 16 pins.
8051 HARDWARE LAB / ECE 2025-26
single bus, four devices, eight strobes
03 / 07

## Slide 4
SLIDE 04 / STACK
Hardware and software stack
Four layers, one board, no operating system
APPLICATION
13 firmware programs / board.h / 01 blink to 13 self test
firmware/src
DRIVER
bus, LED, 7-segment, LCD, ADC, UART, switch debounce
firmware/inc/board.h
INTERFACE
8-bit parallel / HD44780 8-bit / ADC0804 / UART 9600 8N1
P0, P2, P3
SILICON
AT89S52 2x 74HC573 ADC0804 LM35 MAX232 HD44780 BC547 x4 7805
through-hole DIP
AT89S52-24PU
MCU
8 KB flash, 3 timers
74HC573 x2
LATCH
LED bank, segment patterns
ADC0804LCN
ADC
8-bit parallel, 606 kHz
LM35DZ
SENSOR
10 mV per degree C
MAX232N
TRANSCEIVER
TTL to RS-232, 1 uF pump
JHD162A
DISPLAY
16x2 HD44780, 8-bit
BC547 x4
DRIVER
digits, relay, buzzer
L7805CV
REGULATOR
5.00 V, 1 W, heatsinked
Protocol | Pins | Used for
8-bit parallel bus | P0.0-P0.7 | latches, LCD, ADC
UART 9600 8N1 | P3.0-P3.1 | telemetry and shell
SPI (ISP only) | P1.5-P1.7 | flash programming
TOOLCHAIN
Keil uVision 5, C51, level 8, small memory model
USBasp + avrdude -p 8052 USB-RS232 DMM 20 MHz scope
8051 HARDWARE LAB / ECE 2025-26
no RTOS, no external memory, one translation unit per program
04 / 07

## Slide 5
SLIDE 05 / IMPLEMENTATION
Implementation logic and control flow
Interrupt driven display refresh around a polling control loop
board_init
ports, latches, outputs off
display_init
timer 0 at 5 ms, EE00H
adc_read
start, wait INTR, read byte
zone decision
T < 40 / < 70 / >= 70 C
actuate
LEDs, relay, buzzer
publish
LCD, 7-segment, UART 1 Hz
TIMER 0 ISR / EVERY 5 ms
TH0 = EEH TL0 = 00H
seg_tick() alternates the two digits
saves and restores the bus shadow byte
BUS TRANSFER PRIMITIVE
1 save
ea = EA
2 gate
EA = 0
3 place
BUS = v
4 strobe
LE = 1
5 release
LE = 0
6 restore
BUS = shadow
EXTERNAL INTERRUPTS
INT0 falling edge -> emergency latch
INT1 falling edge -> clear the latch
Both ISRs set a flag only; the main loop
does the work, keeping service short.
Stage | Operation | Failure mode handled
Acquire | adc_read, INTR both edges | guarded timeout returns
Convert | T = raw x 25 / 32 integer | no float library needed
Decide | compare at 400 and 700 | emergency overrides all
Actuate | latch write, relay, buzzer | interrupts gated
Publish | LCD, 7-segment, UART 1 Hz | refresh runs in the ISR
Operation | Cycles | Time
machine cycle | 12 osc | 1.0851 us
bus transfer | ~20 | 21.7 us
ADC conversion | - | 114 us
LCD write | ~30 | 32.6 us
display tick | 4608 | 5.000 ms
telemetry period | - | 1.000 s
WHY POLL, WHY INTERRUPT
The display must never flicker, so it runs
in the interrupt. Sensing and acting can
slip by milliseconds, so they poll. Each
mechanism is matched to its own deadline.
8051 HARDWARE LAB / ECE 2025-26
poll in the loop, refresh in the interrupt
05 / 07

## Slide 6
SLIDE 06 / RESULTS
Results, benchmarks and trade-offs
Derived values, measured targets and the decisions behind them
0.00 %
BAUD ERROR
TH1 = FDH at 11.0592 MHz
1.00 kHz
TIMER OUTPUT
FE34H reload, +0.17 %
100 Hz
DISPLAY REFRESH
EE00H reload, per digit
0.78 C
ADC RESOLUTION
7.8125 mV per step
157 mA
BOARD CURRENT
274 mA peak, relay on
3.4 KB
LARGEST PROGRAM
of 8 KB flash, 30 B RAM
Decision | Alternative rejected | Trade-off accepted | Outcome
Shared 8-bit bus | I2C or SPI port expander IC | 8 extra strobes and software arbitration | 54 pins fitted into 32, no extra IC
AT89S52 with ISP | AT89C51, parallel programmer | slightly higher chip cost | programmer cost falls to INR 250
470 Ohm LED resistors | the usual 330 Ohm | about 15 % less brightness | 53 mA per package, inside the 70 mA limit
Vref/2 at 1.000 V | internal 2.5 V reference | one trimpot and one calibration step | 0.78 C per step instead of 1.95 C
Software driven bus | MOVX with an address latch | no hardware address decode | port 2 stays free for eight strobes
Flags inside the ISRs | doing the work in the ISR | one loop of latency | short, predictable service routines
Software debounce | RC filter or Schmitt trigger | 5 ms of loop time | no parts, no spare pins consumed
8051 HARDWARE LAB / ECE 2025-26
20 bench tests, T1-T20, acceptance limits in hardware/TESTING.md
06 / 07

## Slide 7
SLIDE 07 / OUTLOOK
Scalability, future scope and conclusion
Where the architecture has headroom and where it does not
NOW
Single board, verified
13 programs, 20 tests
INR 985 per board
9600 baud telemetry
NEXT
Recover two pins
LCD on a PCF8574 backpack
frees P2.3 and P2.4
adds I2C: RTC, EEPROM
LATER
Multi-node and PCB
RS-485 or ESP-01 link
KiCad two layer layout
mains rated enclosure
CONCLUSION
A 22 pin deficit was closed by architecture, not by extra silicon.
Every constant derives from the 1.0851 microsecond machine cycle.
Thirteen programs compile clean; the build is staged and measured.
Every hardware result reconciles with the phase 1 simulator.
SCALABILITY LIMITS
Bus
shared P0 caps throughput, a few hundred kHz
ADC
one channel, 8-bit, about 114 us per sample
Memory
256 B RAM, no external data memory wired
Interrupts
two external sources, no priority nesting
Relay
demonstration only, never mains connected
8051 HARDWARE LAB / ECE 2025-26
repository: AdityaRezan/8051-hardware-lab
07 / 07